Small Airliner Study 2021 – 22
The information in this document is the property of Dr F A Hewitt and is provided for students of the University of Bristol to carry out a Design Project. It may not be divulged to third parties or copied other than for purposes associated with the project.
Engine Information
The project engines for 2021-22 are a generic high-bypass turbofan engine and a similarly thrust-scaled turboprop both defined at matched technology level appropriate for 2027 Technology Availability Date. The Table below gives an overview of the engines for this study. Note that data has also been provided for hydrogen fuelled variants of both engines. See the next section for notes on hydrogen fuelling.
	TF 15	TP 14
Thrust SLS ISA + 15K Lb	15,000	14,070
Shaft Power SLS kW		4745
Mach Number Altitude	M=0.8 35k	M = 0.7 30k
SFC kg/hr/N (at Mn & Alt above)	0.061	0.051
Fan Diameter mm	1250
Propeller Diameter m		4.78
Number of blades		6
Total Prop Mass (inc Pylon)	2527	2625
T/(M*9.81)	2.7	2.4
Power/Mass kW/kg)		4.1

Use of Hydrogen Fuel
Many aspects of the aircraft and its powerplant change if hydrogen is to be used. For this project, it is assumed that the hydrogen will be stored as cryogenic liquid para-hydrogen at around 20 K, and density of around 70 kg/cubic metre. Ultimately, choices will have to be made about whether the cooling potential of the liquid fuel will be used by the aeroplane or the engines, or both, and to what extent. This data assumes that the cryogenic liquid will simply be delivered by the boost pumps to the airframe/engine interface at close to storage temperature – the engine will then pump the liquid to injection temperature, and will use some of the cooling potential for duties such as oil cooling, and to pre-cool the turbine cooling air, before injecting the now-gaseous fuel into the engine combustion chamber. The nature of the gaseous injection means that the fuel may be pumped to a considerably lower injection pressure than is necessary for liquid kerosene – this is fortunate, as pressurising the cryogenic liquid demands more complex pump design, anyway.
There are some “interesting” problems to be overcome in achieving flow stability in heat exchange systems with change of state from liquid to gas. You do not need to deal with this issue – it will be a problem for the engine designers – consider yourselves fortunate! The different exhaust gas products change heat transfer and work characteristics somewhat, compared to kerosene, but the overall effects of the changes is to return the engine performance to a very similar level to the conventional unit. Given the possible variations on the theme, the performance data provided basically reflects the difference in the Lower Heating Values of the two fuels per kilogramme, i.e. hydrogen mass flow to match the kerosene performance point. The changes to the engines associated with the fuel change will be almost entirely within the nominal engine size and shape envelope, and the c.g. can be considered unchanged. The different fuel pumping and the additional equipment required, in the form of different heat exchangers and insulated pipework, will add some mass to the powerplant, but this penalty will be quite small. For the purpose of this study, an extra mass penalty of 20 kg should be assumed for both the turboprop and turbofan variants, with this mass addition scaling linearly with the thrust scale eventually chosen.
Performance Data
Note the engine performance supplied in the Excel Spreadsheet is in the form of “fully installed” Thrust and Fuel Flow for both the Turbofan and Turboprop. Thrust is defined as all the forces within the inlet and exit stream-tubes and the effect of power and other offtakes suitable for this class of aircraft have been included. In the case of the Turboprop lift gains and drag losses associated with the propeller wash over wing or other surfaces are not included as they are concept specific, nor are the external drags of the engine nacelles for either engine type. This area is a prime area for missed or double accounting, between powerplant and aero specialists. Make specific arrangements to avoid this error.

Turbofan engine
Baseline Engine is 66.7 kN ISA+15K sea-level static take-off thrust.
High-bypass design – typical bypass ratio around 12:1.
Short-cowl unmixed exhaust
Engine mounting to the aircraft pylon:- attachment locations are to the top of the fan case for thrust and weight, and to both sides of the top of the LP turbine case for weight, balance and stabilisation against sway. The rear mounting design includes provision to allow axial expansion and contraction of the engine with temperature, relative to the pylon.
Bare engine can be treated as rotationally symmetric apart from the power offtake drive, for the purposes of this study.
Podded engine form is also externally rotationally symmetric – though the pod detail form can be adjusted for optimum airframe integration by agreement with your advisor.
The engine provides offtake power by a single shaft driven from the engine intermediate shaft – this is assumed to drive electrical generator(s) in an all-electric aircraft configuration. Generators for this mission typically 90kW unit on each engine.

Mass and Size
Powerplant Masses for 66.7 kN ISA+15K static take-off thrust Engine.
Bare Engine	1464 kg
Pod Systems	659 kg
Pylon System	366 kg

Total single powerplant mass on wing	2489 kg
Powerplant dimensions.
Podded engine overall length	3.889 m
Maximum pod diameter	1.732 m
Distance of c.g. aft from bare engine face	0.990 m
Centre of gravity axial location is for the bare engine. The c.g. location may move forward by approx 250mm when the engine is installed in the pod with its systems. Pylon mass is dependent on engine position relative to the wing and is indicative only.
Turboprop Engine
The design configuration and layout of the powerplant is as for a turbomachine driving a separately cased two-stage propeller reduction gearbox. The centre of gravity of the engine, gearbox and propeller system is at the inlet face of the turbomachine. This scale and style of turboprop engine is very widely deployed in current service. Airframe electrical generator is typically driven from the PGB rear face.
Powerplant Masses for Datum Turboprop Engine (4745 kW)
Basic engine, PGB and propeller =	1483 kg
(Max Power (kW) / 3.2) kg;
Mounting frame structure,	593 kg
nacelle, nacelle systems &
anti-vibration mount system (40% of (1))
Pylon System Mass	415 kg
(20% of (1) + (2))
Total Mass on wing	2491 kg
 (Sum of (1), (2) and (3))
Powerplant Dimensions for Datum Engine.
Overall length	4.547 m
Distance of c.g. from propeller spinner tip	2.273 m
Propeller Diameter in m =	4.78 m
{(Max Power kW)/ (11 x No. Blades x π)} 0.5
Note also that the c.g. lengthwise location is for the engine, PGB & propeller. Nacelle shapes vary, depending on installation design, and the mass for the nacelle and mounting systems is merely typical. Pylon mass is again representative and depends strongly on the positioning of the powerplant relative to the wing attachment points.
Performance Scaling Effects
For any given engine configuration, larger internal flow areas result in smaller proportionate internal losses due to friction and turbulence at blade hub and tip boundary layer areas. This effect is most marked for growth from the smallest sizes, and tends to “wash out” as size increases. (Reducing proportion of boundary layers to total flow).
In consequence, engine efficiency tends to improve as size increases, hence actual fuel flow and SFC reduce for increasing scale, and rise for reducing scale, relative to the nominal mid-sized engine.
Turboprop Data - General
Nominal Maximum Power = 4745 kW.
Propeller torque reaction is up to 66 kN.m in normal operation.
The two-spool core drives a free power turbine on the third shaft with output to offset reduction propeller gearbox (PGB). Starter/generator on engine core.
Major accessory loads including main electrical generators are mounted on/driven by the PGB. Also mounts propeller pitch control pump and actuator system.
Separate electrically-driven pump mounted on PGB for emergency propeller feathering following engine shut down.
A propeller brake would be installed to prevent free wind-milling when parked.
Propeller is a 6-blade unit with pitch-lock or centrifugal pitch/speed control.
Engine mounting is by anti-vibration mounts to the aircraft mount frame on both sides and top of the Propeller Gearbox (PGB), with the rear mount to the frame on both sides of the top of the low pressure turbine casing.
Size and Mass Scaling Effects
Ensure “pinch-points” thrust requirements (e.g. Top-of-Climb / Start-of-Cruise and Emergency cases) have been correctly identified before defining thrust scaling factor.
Thrust scales with airflow – hence with inlet and compressor frontal area
All thrust cases at all altitudes scale by the engine compressor frontal area scale factor
Scale linear dimensions of the core engine and PGB as thrust change ratio to 0.5 power.
Mass Scaling Effects
A simplified scaling rule is used as follows:
Basic engine, PGB and propeller = (Max Power (kW) / 3.2) kg;
1. Mounting frame structure, nacelle, nacelle systems & anti-vibration mount system equal to 40% of (1);
2. Pylon System Mass equals 20% of ((1) + (2)).
Total Mass on wing equals sum of (1), (2) and (3).

Performance effects of thrust scale
Turboprop sensitivity of SFC to thrust and physical scale is smaller than for the turbofan, over the range of plus/minus 20% scale from the nominal engine provided and the SFC change can be ignored for the purpose of this study.

See also : Sections of: Turbofan Engine, Turbofan in Nacelle & Turboprop Drawings:-
2021 – 2022 Engine Sections.ppt
Engine Performance supplied in separate Excel Spreadsheet